Robot
300Mbps
Field Computer
10K~2Kbps/300Mbps*
50Mbps
Operator Computer
Operator Cloud

---
1 sec burst in 300Mbps/0 latency
1 time per 1~30sec
10K~2Kbps
10K~2Kbps

---
Packet P
1 sec latency
A
B
1 sec latency
2 sec latency from application layer
ACK

---
Data
Application
TCP or UDP
Header
(20 or 8 bytes)
Transport
IP Header
(20 bytes)
Internet
Frame
Header
(14 bytes)
Frame
Footer
(4bytes)
LINK